## Slide 1: A REPORT ONMATLAB ASSIGNMENT THREE
Numerical Methods for Engineering Applications
Presented By: Group 5
Course: Computer Programming
Lecturer: Mr. Maseruka Benedicto
Date: 1st October, 2025

## Slide 2: GROUP MEMBERS
NAME | REGISTRATION NO | COURSE
Kemigisa Tasha Caroline | BU/UG/2024/5056 | AMI
Ayebare Prudence | BU/UP/2024/1022 | WAR
Kenyi Moses | BU/UP/2024/5344 | MEB
Zzimbe Enock | BU/UP/2024/4455 | WAR
Oketch Simon | BU/UP/2024/0841 | AMI
Nakyagaba Barbra | BU/UP/2024/4328 | APE
Kabugiri Pearl Flavia | BU/UP/2024/4450 | WAR
Omali Emmanuel | BU/UP/2024/1062 | WAR
Oyugi Andrew Linus | BU/UP/2024/1068 | WAR
Kagogya Ann Lauriene | BU/UP/2024/0996 | PTI

## Slide 3: PROJECT OVERIEW AND OBJECTIVES
Objectives: Utilize knowledge of algorithms and control structures to solve numerical problems
Keys tasks
Implement numerical methods for finding roots of functions
Implement numerical methods for solving differential equations
Apply these methods to practical, real-world problems.
Requirement: Compare at least two different methods on similar problems, analyzing both solution accuracy and computation time.

## Slide 4: REAL-WORLD PROBLEMS ADDRESSED
Problem 1: Projectile Motion
Goal: Find a projectile hits the ground.
Equation: h(t) = -4.9t squared + 15t + 10 = 0
Parameters: -4.9: Half gravitational acceleration (g/2)
15: initial velocity (m/s)
10: initial height (m)

## Slide 5: IDEAS GAS VOLUME
Goal: Find the molar volume where pressure approaches zero (van der Waals approximation).
Equation: f(v) = v cubic – 0.165v squared + 0.000136 = 0
Context: Models gas behavior under extreme conditions in thermodynamics.

## Slide 6: METHODS USED – ROOT FINDING
We compared two numerical methods for finding roots.
Bisection Method
Principle: Uses interval halving. Requires two points [a, b] where f(a)*f(b) < 0.
Pros: Guaranteed to converge, simple and robust.
Cons: Slow (linear convergence)
2. Newton-Raphson Method
Principle: Uses function derivative to find tangents and converge to the root.
Pros: Very fast (quadratic convergence).

## Slide 7: BISECTION METHOD- RESULTS AND ANALYSIS
Projectile Problems:
Root: t = 3.624 seconds
Iteration: 19
Final error: 1. 1e-5meters
Gas volume Problem:
Root: V = 0.15967 squared/mol
Iteration: 10
Final error: 6.59e-8
Key observation: Reliable and consistent convergence for both problems, as theoretically excepted.

## Slide 8: NEWTON-RAPHSON METHOD- RESULTS AND ANALYSIS.
Projectile motion
Root: t = 3.624 seconds
Iterations: 5
Final error: 1.0e- 12
Gas volume problem:
Root: V = 0.15967m squared/mol
Iteration: 3
Final error: 2.81e- 10
Key Observation: significantly faster convergence than the Bisection Method, with much higher accuracy in fewer iterations

## Slide 9: METHODS USED- SOLVING DIFFERENTIAL EQUATIONS
We compared two numerical methods for solving ODE’s:
Euler’s method
Principle: First order method, uses slope at the current point to estimate the next.
Pros: Simple to understand and implement.
Cons: less accurate, can be unstable for larger step sizes
2. Runge-Kutta (4th order)
Principle: Uses a weighed average of four slopes within each step.
Pros: Much more accurate and stable than Euler’s method.
Cons: Computationally more expensive per step.

## Slide 10: EULER’S METHOD
Application 1: car suspension system
Model: Spring-Mass-Damper: my + cy + ky = 0
Parameters: mass m=1000kg, spring k=2000 N/m, Damper c=2000 N.s/m
Results: Simulated the oscillatory response to bump, calculating maximum displacement and settling time
Application 2: Free Fall with Air Resistance
Model: Newton’s 2nd Law with drag force.
Parameters: Mass m=8okg, Drag Coefficient c=0.24
Results: Simulated descent from 3000m, calculating impact velocity and time to ground.

## Slide 11: RUNGE-KUTTA METHOD APPLICATIONS
Application 1: Projectile Motion with Drag
Model: 2D motion with air resistance.
Parameters: launch at 45 degrees,v0=50 m/s
Results:
Max height: 63.63 m
Range: 254.46 m
Flight Time: 7.21 s
Application 2: Car Suspension System
Model: Same Spring-Mass-Damper system as with Euler’s method.
Purpose: To compare the accuracy and stability with the Euler’s solution

## Slide 12: COMPARATIVE ANALYSIS AND KEY FINDINGS
Method | Accuracy | Speed/convergence | Stability | Best for
Bisection | Good | Slow(Linear) | Very high | Robust, simple starts
Newton Raphson | Excellent | Very fast (Quadratic) | Medium | When derivative is available
Euler’s | Low | Fast per step | Low | Quick, simple estimates
Runge-kutta 4 | High | Slower per step | High | Accurate simulations

## Slide 13: CHALLENGES AND LEARNING OUTCOMES
Challenges:
Translating mathematical algorithms into efficient MATLAB code.
Debugging logical errors in loops and conditional statements.
Ensuring results from different methods were consistent and valid.
Learning outcomes
Enhanced practical understanding of numerical methods.
Improved skills in algorithm development and MATLAB programming
Gained experience in comparing computational techniques.
Strengthened collaborative problem-solving and teamwork.

## Slide 14: CONCLUSION
Successfully implemented and compared multiple numerical methods (Bisection, Newton-Raphson, Euler,Runge-Kutta) in MATLAB
Effectively applied these methods to solve realistic engineering problems from projectile dynamics to thermodynamic systems.
The project demonstrated that there is no single “best” method; the optimal choice depends on the specific problem requirements foe speed, accuracy, and stability.
The assignment was a valuable exercise in computational thinking ,coding, and collaborative work